## Slide 1: Logic Gates
Course Code: CSC 1101
Dept. of Computer Science
Faculty of Science and Technology
Lecturer No: | 09 | Week No: | 09 | Semester: | 
Lecturer: | Name & email |  |  |  | 
Course Title: Introduction to Computer Studies

## Slide 2: Lecture Outline
Understanding Logic Gate and the use of these.

## Slide 3: Specific Objectives
Logic gates
Logic circuits and Boolean expressions
Combinational circuits and design

## Slide 4: Logic Gate
Logic gates are electronic circuits that operate on one or more input signals to produce standard output signal
Are the building blocks of all the circuits in a computer
Some of the most basic and useful logic gates are AND, OR, NOT, NAND and NOR gates

## Slide 5: AND Gate
Physical realization of logical multiplication (AND) operation.
Generates output signal of 1 only if all input signals are also 1

## Slide 6: AND Gate (Block Diagram Symbol and Truth Table)

## Slide 7: OR Gate
Physical realization of logical addition (OR) operation
Generates an output signal of 1 if at least one of the input signals is also 1

## Slide 8: OR Gate (Block Diagram Symbol and Truth Table)

## Slide 9: NOT Gate
Physical realization of complementation operation
Generates an output signal, which is the reverse of the input signal

## Slide 10: NOT Gate (Block Diagram Symbol and Truth Table)

## Slide 11: NAND Gate
Complemented AND gate
Generates an output signal of:
1 if any one of the inputs is a 0
0 when all the inputs are 1

## Slide 12
NAND Gate (Block Diagram Symbol and Truth Table)

## Slide 13: NOR Gate
Complemented OR gate
Generates an output signal of:
  1 only when all inputs are 0
  0 if any one of inputs is a 1

## Slide 14: NOR Gate (Block Diagram Symbol and Truth Table)

## Slide 15: Logic Circuits
When logic gates are interconnected to form a gating / logic network, it is known as a combinational logic circuit
The Boolean algebra expression for a given logic circuit can be derived by systematically progressing from input to output on the gates
The three logic gates (AND, OR, and NOT) are logically complete because any Boolean expression can be realized as a logic circuit using only these three gates

## Slide 16
B C
A
A
NOT
OR
B + C
D= AB + C
AND
Finding Boolean Expression of a Logic Circuit(Example 1)

## Slide 17
A B
NOT
C=A +BAB
A B
AND
A  B
AB
AND
Finding Boolean Expression of a Logic Circuit(Example 2)
OR

## Slide 18
Constructing a Logic Circuit from a Boolean Expression (Example 1)

## Slide 19
Constructing a Logic Circuit from a Boolean Expression (Example 2)

## Slide 20
Universal NAND Gate
To understand this, consider:
  Basic logic gates (AND, OR, and NOT) are logically complete
  Sufficient to show that AND, OR, and NOT gates can be implemented with NAND gates
Nand gate is an universal gate, I is alone sufficient to implement
any Boolean expression

## Slide 21: Implementation of NOT, AND and OR Gates by NAND Gates
(a) NOT gate implementation.
A
A  A = A + A = A
(b) AND gate implementation.
A  B  A B
A B
A B
(Continued on next slide)

## Slide 22: Implementation of NOT, AND and OR Gates by NAND Gates (Continued from previous slide..)
A B  A + B  A  B
A
B
A  A =A
B B =B
(c) OR gate implementation.
and OR Gates by

## Slide 23: Method of Implementing a Boolean Expression with Only NAND Gates
Step 1: From the given algebraic expression, draw the logic diagram with AND, OR, and NOT gates. Assume that
inputs are
both the normal available
Step 2:
Draw a second logic diagram with the equivalent NAND logic substituted for each AND, OR, and NOT gate
Step
3: Remove diagram
all pairs of cascaded inverters from the as double inversion does not perform any
function. Also remove inverters
logical
single external inputs
and complement
connected to
the
corresponding input variable
(A) and complement (A)

## Slide 24: Implementing a Boolean Expression with Only NAND Gates (Example)
Boolean Expression =
(a) Step 1: AND/OR implementation
B D A
C
AB
A
B
A +BD
BD
CA +BD
A  B + C A + B D 
A  B + C A + B D 
(Continued on next slide)

## Slide 25: Implementing a Boolean Expression with Only NAND Gates (Example) (Continued from previous slide..)
(b) Step 2:
AND
OR
OR
5
3
4
AND
B D
2
A
C
1
A B
AB
A+BD
A B + CA+BD
CA+BD
AND
BD
Substituting equivalent NAND functions
(Continued on next slide)

## Slide 26: Implementing a Boolean Expression with Only NAND Gates (Example) (Continued from previous slide..) (
(c) Step 3:
NAND implementation.
A B + CA +BD
A
C
A
1
B
B D
2
3
4
5

## Slide 27: Universal NOR Gate
NOR gate is an universal gate, it is alone sufficient to implement any Boolean expression
To understand this, consider:
  Basic logic gates (AND, OR, and NOT) are logically complete
  Sufficient to show that AND, OR, and NOT gates can be implemented with NOR gates

## Slide 28: Implementation of NOT, OR and AND Gates by NOR Gates
(a) NOT gate implementation.
A
A  A = A  A = A
(b) OR gate implementation.
A  B  A  B
A  B
A B
(Continued on next slide)

## Slide 29: Implementation of NOT, OR and AND Gates by NOR Gates (Continued from previous slide..)
A
B
A  A =A
A + B  A B  A B
B  B =B
(c) AND gate implementation.

## Slide 30
diagram with AND, OR, and NOT gates. Assume that
and complement
inputs are
Step 2:
Draw a second logic diagram with equivalent NOR logic substituted for each AND, OR, and NOT gate
Step 3:
Remove all parts of cascaded inverters from the diagram as double inversion does not perform any
logical function. Also remove inverters single external inputs and
complement
connected to
the
corresponding input variable
A
both the normal A
available
Method of Implementing a Boolean Expression with Only NOR Gates
Step 1: For the given algebraic expression, draw the logic

## Slide 31: Implementing a Boolean Expression with Only NOR Gates (Examples)(Continued from previous slide..)
B D A
C
A
B
(a) Step 1: AND/OR implementation.
A +BD
BD
CA +BD
A B + CA +BD
=
AB
Boolean Expression A B + CA +BD
(Continued on next slide)

## Slide 32
(b) Step 2:
2
B
D
B
AND
OR
5
6
4
AN
D
OR
3
A
C
BD
C A +BD


A  B + C A +BD
A +BD
Substituting equivalent NOR functions.
(Continued on next slide)
A
AND

## Slide 33: Implementing a Boolean Expression with Only NOR Gates (Examples)(Continued from previous slide..)
B
D
A C
(c) Step 3:
NOR implementation.
A B + CA +BD
A B
3
4
5
1
2
6

## Slide 34: Exclusive-OR Function
A  B = A  B + A  B
C = A B = A B+ A B
C = A B = A B+ A B
A B
A 
B
Also, A B C = A  B  C = A B  C
(Continued on next slide)

## Slide 35: Exclusive-OR Function (Truth Table)
Inputs |  | Output
A | B | C = A B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
(Continued from previous slide..)

## Slide 36
A B
C = A © B = A B+ A B
Also, (A © B) © = A © (B © C) = A © B © C
Equivalence Function with Block Diagram Symbol
(Continued on next slide)
A © B = A  B+ A  B

## Slide 37: Equivalence Function (Truth Table)
Inputs |  | Output
A | B | C = A © B
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 38: Steps in Designing Combinational Circuits
State the given problem completely and exactly
Interpret the problem and determine the available input variables and required output variables
Assign a letter symbol to each input and output variables
Design the truth table that defines the required relations between inputs and outputs
Obtain the simplified Boolean function for each output
Draw the logic circuit diagram to implement the Boolean function

## Slide 39: Designing a Combinational Circuit Example 1 – Half-Adder Design
S = AB+ AB C = AB
Boolean functions for the two outputs.
Inputs |  | Outputs | 
A | B | C | S
0 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0

## Slide 40: Designing a Combinational Circuit Example 1 – Half-Adder Design(Continued from previous slide..)
Logic circuit diagram to implement the Boolean functions
A
B
A B
S = AB+ AB
C = AB
A
B
AB
AB

## Slide 41: Designing a Combinational Circuit Example 2 – Full-Adder Design
Truth table for a full adder
Inputs |  |  | Outputs | 
A | B | D | C | S
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1
(Continued on next slide)

## Slide 42: Designing a Combinational Circuit Example 2 – Full-Adder Design(Continued from previous slide..)
= AB+ AD+BD
(when simplified)
Boolean functions for the two outputs:
S = ABD+ ABD+ ABD+ ABD C = ABD+ ABD+ ABD+ ABD
(Continued on next slide)

## Slide 43: Designing a Combinational Circuit Example 2 – Full-Adder Design(Continued from previous slide..)
A B
D
A
A B
B
D
A
B D
S
A B D
A B D
A B D
A B D
D
(a) Logic circuit diagram for sums
(Continued on next slide)

## Slide 44: Designing a Combinational Circuit Example 2 – Full-Adder Design(Continued from previous slide..)
C
A  B
A  D
B  D
A B
A D
B D
(b) Logic circuit diagram for carry

## Slide 45: Key Words/Phrases
Absorption law
AND gate
Associative law
Boolean algebra
Boolean expression
Boolean functions
Boolean identities
Canonical forms for Boolean functions
Combination logic
circuits
Cumulative law
Complement of a function
Complementation
De Morgan’s law
Distributive law
Dual identities
Equivalence function
Exclusive-OR function
Exhaustive enumeration method
Half-adder
Idempotent law
Involution law
Literal
Logic circuits
Logic gates
Logical addition
Logical multiplication
Maxterms
Minimization of Boolean functions
Minterms
NAND gate
NOT gate
Operator precedence
OR gate
Parallel Binary Adder
Perfect induction method
Postulates of Boolean algebra
Principle of duality
Product-of-Sums expression
Standard forms
Sum-of Products expression
Truth table
Universal NAND gate
Universal NOR gate

## Slide 46: References
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha

## Slide 47
Thank you